Bin Fan Controller                                                                       3/15/2020

The unit has been designed to control grain bin fans. It has been designed around the Corn Moisture Equilibrium Chart in that it looks at the outside

temperature and humidity. The operator sets the limits on each and the

controller will run the fan as long as the temperature and humidity is within

the limits set.

The Controller can be powered from 110v, 220v single and three phase.

The output is wired to a starter / contactor on the fan to be controlled.

The Controller can only be used with fans which have a starter / contactor.

A toggle switch is required to be installed in the fans start circuit. This

enables the fan to be put in Auto or Manual Mode.

Operation is simple;

Turn power switch on Controller

Set Humidity Upper Limit

Set Temperature Lower Limit

Save Settings

If the fan is not running the display will tell you the reason and guide

you to adjust the Temperature / Humidity if desired.

The Controller will run the fan as long as the temperature and humidity

are within the set points.

The Controller will keep track of the D/H/M (Days/Hours/Minutes that the

fan has ran. The Controller stores the Limits, Days, Hours, and

Minutes every 24 hours.

In the event of a power failure the Controller will restore the information and continue to operate after power is restored.

There are numerous displays / Settings that are available via the keypad.

A Menu is provide inside the door of the Controller as well as from the

keypad and display.